## Slide 1
ELECTRICAL SCIENCE-1
(15B11EC111)
Unit-4
Sinusoidal Steady State Analysis
( Physical Model for a Sinusoid, Average Value, Effective Value, Phasor presentation, Addition of Phasor using Complex Numbers, Concepts of impedance and admittance. )
Lecture-1
Dr. Abhishek Kashyap
Assistant Professor (Senior Grade, JIIT Noida)

## Slide 2: Topics to be covered
DC and AC Currents.
A Sinusoid.
 Some Definitions.
 Phase Difference.
 Physical Model for a Sinusoid.
Average of a sine wave.
RMS or Effective Value.
Concept of Phasors.
 Operations on Phasors.
Additions of Phasors
Using Complex Numbers.
Power and Power Factor.
Purely Resistive Circuit.
Purely Inductive Circuit.
 Inductive Reactance.
Purely Capacitive Circuit.
 Capacitive Reactance
2

## Slide 3: DC and AC Currents
Difference between
In dc circuits, when a current of 3 A adds to another current of 4 A, the net current is always 7 A.
However, an ac current of 3 A when added to another ac current of 4 A can result anything between 1 A and 7 A, depending upon their relative phase.
It is similar to adding a force of 3 N to another force of 4 N. The result is not necessarily a force of 7 N. It be anything between 1 N to 7 N, depending on their relative directions. These are added vectorially.
3

## Slide 4
Does it mean that KCL does not apply to AC Circuits ?
Ans. :Yes, it does apply. However, the ac currents are added in a Phasor Diagram.
I  I1  I 2
4

## Slide 5: A Sinusoid
(a) Current i versus angle ωt. (b) Current i versus time t.
i  Im sint
5

## Slide 8: Some Definitions
T
Amplitude (or peak value) : It is the maximum value, positive or negative, of an alternating quantity.
Instantaneous Value : It is the value of the quantity at any instant.
Time period (T) : It is the duration of one complete cycle.
Frequency (f) : It is the number of cycles that occurs in one second.
f  1

## Slide 9
Angular Frequency : Angular frequency, denoted as ω, is equal to the number of radians covered in one second. Its unit is rad/s. Since one cycle covers 2π radians and there are f cycles in one second, the angular frequency is given as
T
  2πf
  2π
or

## Slide 10
Phase : It is the fraction of the time-period or cycle that has elapsed since it last passed from the chosen zero position or origin. The phase at time t from the chosen origin is given by t/T.
Phase angle : It is the equivalent of phase expressed in radians or degrees. It is denoted as θ. Thus, phase angle, θ = 2πt/T.
Phase difference : It is the angular displacement between two alternating quantities.
10

## Slide 11: A rotating bar generates a sinusoidal wave.
11

## Slide 12: Physical Model for a Sinusoid
(a) A rotating crank. (b) Sinusoidal waveform.
The vertical projection of the rotating crank is its length times the sine of the angle θ.
12

## Slide 13: Phase Difference
(a) Displacement by to the left
(b) Displacement by 
to the right
It has become normal practice in electrical engineering to express ωt in radians and the angle in degrees.

## Slide 14
(c) Displacement
by 90° to the left.
(d) Displacement
by 180°.
Note that the resulting position of the waveform is the same whether the phase shift is 180° (π rad) to the left, or 180° to the right.

## Slide 15: Example 1
A sinusoidal voltage is 20 V peak-to-peak, has a time of 5 ms between consecutive peak and trough, and at t = 0 is -3.6 V and decreasing. Find the equation for the instantaneous value of the voltage, and the value
of the voltage at t = 12 ms.
NOTE : First draw the waveshape, then start the solution.

## Slide 16
Solution :
1
10 103
T  2 5 ms  10 ms;
2
2
 20 10 V;
1
 100 Hz
T 10 ms
 f  1 
 Vp p
m
V

   2f  2π100  628.3 rad/s.
Therefore, the sinusoid voltage is of the form
v  10sin(628.3t ) V
Now, we are given that at t = 0, v = -3.6 V. Putting these values, we get

## Slide 17: or sin  0.36 or 338.9
 3.6  10sin()
   158.9
As shown in figure, the given sinusoid is shifted to
right by angle , which is less than 180°.
Also, we know that shifting rightward means there is a lag of angle . Therefore, the equation of the given sinusoidal voltage is
v 10sin(628.3t 158.9) V

## Slide 18: The value of voltage at 12 ms,
π
v(t  0.012s)  10sin  628.3 0.012  180 158.9V
 


 10sin 432 158.9 V  9.985 V

## Slide 19
Thanks