## Slide 1
Digital Circuit Design
18B11EC215
Lecture 7
Implementation using Logic Gates and
Standard forms

## Slide 2: Outline
Universal Gates: NAND and NOR
Implementation using NAND Gates
Implementation using NOR Gates
Standard Forms
Minterm & Maxterm
Canonical Form
  SOP
  POS
Conversion between canonical forms

## Slide 3: Universal Gates: NAND and NOR[1,3]
AND/OR/NOT gates are sufficient for building any Boolean functions.
We call the set {AND, OR, NOT} a complete set of logic.
However, other gates are also used because:
(i) usefulness
(ii) economical on transistors
(iii) self-sufficient
NAND/NOR: economical, self-sufficient
XOR: useful (e.g. parity bit generation)

## Slide 4: NAND Gate
NAND gate is self-sufficient (can build any logic circuit with it).
Therefore, {NAND} is also a complete set of logic.
Can be used to implement AND/OR/NOT.
Implementing an inverter using NAND gate:
(x.x)' = x' (T1: idempotency)
x
x'

## Slide 5: NAND Gate[2]
((xy)'(xy)')' = ((xy)')' idempotency
= (xy) involution
((xx)'(yy)')' = (x'y')' idempotency
= x''+y'' DeMorgan
= x+y involution
Implementing AND using NAND gates:
Implementing OR using NAND gates:
x
x.y
y
(x.y)'
x
x+y
y
x'
y'

## Slide 6: NOR Gate[2]
NOR gate is also self-sufficient.
Therefore, {NOR} is also a complete set of logic
Can be used to implement AND/OR/NOT.
Implementing an inverter using NOR gate:
(x+x)' = x' (T1: idempotency)
x
x'

## Slide 7: NOR Gate[2]
((x+x)'+(y+y)')'=(x'+y')' idempotency
= x''.y'' DeMorgan
= x.y involution
((x+y)'+(x+y)')' = ((x+y)')' idempotency
= (x+y) involution
Implementing AND using NOR gates:
Implementing OR using NOR gates:
x
x+y
y
(x+y)'
x
x.y
y
x'
y'

## Slide 8: Implementation using NAND gates[1,2,3]
Possible to implement any Boolean expression using NAND gates.
Procedure:
(i) Obtain sum-of-products Boolean expression:
e.g. F3 = xy'+x'z
(ii) Use DeMorgan theorem to obtain expression using 2-level NAND gates
e.g. F3 = xy'+x'z
= (xy'+x'z)' ' involution
= ((xy')' . (x'z)')' DeMorgan

## Slide 9: Implementation using NAND gates contd.
F3 = ((xy')'.(x'z)') ' = xy' + x'z
x'
z
F3
(x'z)'
(xy')'
x
y'

## Slide 10: Implementation using NOR gates[1,2,3]
Possible to implement any Boolean expression using NOR gates.
Procedure:
(i) Obtain product-of-sums Boolean expression:
e.g. F6 = (x+y').(x'+z)
(ii) Use DeMorgan theorem to obtain expression using 2-level NOR gates.
e.g. F6 = (x+y').(x'+z)
= ((x+y').(x'+z))' ' involution
= ((x+y')'+(x'+z)')' DeMorgan

## Slide 11: Implementation using NOR gates contd.
F6 = ((x+y')'+(x'+z)')' = (x+y').(x'+z)
x'
z
F6
(x'+z)'
(x+y')'
x
y'

## Slide 12: Standard Forms
Two Standard Forms:
Sum-of-Products and Product-of-Sums
Literals: A variable and its complemented form
x, x' , y, y'
Product Term: A single literal or a Product of several literals
x, x.y.z', A'.B, A.B
Sum Term: A single literal or a Sum of several literals
x, x+y+z', A'+B, A+B

## Slide 13: SOP and POS
Sum-of-Products (SOP) Expression:
A product term or a logical sum (OR) of several product terms.
x,
x+y.z',
x.y'+x’.y.z,
A.B+A'.B'
Product-of-Sums (POS) Expression:
A sum term or a logical product (AND) of several sum terms.
x,
x.(y+z'),
(x+y').(x'+y+z),
(A+B).(A'+B')
Every Boolean expression can either be expressed as SOP or POS expression.

## Slide 14: Example
x.y + x.y + x.y.z
(x + y).(x + y).(x + z)
x + y + z or x.y.z
4. x.(w + y.z) or z + w.x.y + v.(x.z + w)
SOP
POS
Both
Neither
SOP circuits can easily be implemented using NAND Gate
POS circuits can easily be implemented using NOR Gate

## Slide 15: Minterm & Maxterm [1,2]
Consider two binary variables x, y.
Each variable may appear as itself or in complemented form as literals (i.e. x, x' & y, y' )
For two variables, there are four possible combinations with the AND operator, namely:
x'.y', x'.y, x.y', x.y
Minterm: a product term in which all the variables appear exactly once, either complemented or uncomplemented
These product terms are called the minterms.
A minterm of n variables is the product of n literals from the different variables.

## Slide 16: Minterm & Maxterm [1,2]
In general, n variables can give 2n minterms.
In a similar fashion, a maxterm of n variables is the sum of n literals from the different variables.
Examples: x'+y', x'+y, x+y',x+y
Maxterm: a sum term in which all the variables appear exactly once, either complemented or uncomplemented
In general, n variables can give 2n maxterms.

## Slide 18: Canonical Form: Sum of Minterms[1]
What is a canonical/normal form?
  A unique form for representing something.
Any Boolean function F( ) can be expressed as a unique sum of minterms and a unique product of maxterms (under a fixed variable ordering).
In other words, every function F() has two canonical forms:
  Canonical Sum-Of-Products (sum of minterms)
  Canonical Product-Of-Sums (product of maxterms)

## Slide 20: Conversion of SOP from standard to canonical form [1]
Expand non-canonical terms by inserting equivalent of 1 in each missing variable x: (x + x’) = 1
Remove duplicate minterms
f1(a,b,c) = a’b’c + bc’ + ac’ = a’b’c + (a+a’)bc’ + a(b+b’)c’ = a’b’c + abc’ + a’bc’ + abc’ + ab’c’ = a’b’c + abc’ + a’bc’ + ab’c’
= m1+m6+m2+m4

## Slide 21: Canonical Form: Product of Maxterms [1]
Maxterms are sum terms.
For Boolean functions, the maxterms of a function are the terms for which the result is 0.
Boolean functions can be expressed as Products-of-Maxterms.

## Slide 23: Conversion of POS from standard to canonical form
Expand noncanonical terms by adding 0 in terms of missing variables (e.g., x.x’ = 0) and using the distributive law
Remove duplicate maxterms
f1(a,b,c) = (a+b+c)•(b’+c’)•(a’+c’) = (a+b+c)•(aa’+b’+c’)•(a’+bb’+c’) = (a+b+c)•(a+b’+c’)•(a’+b’+c’)•(a’+b+c’)•(a’+b’+c’) = (a+b+c)•(a+b’+c’)•(a’+b’+c’)•(a’+b+c’)

## Slide 24: Conversion Between Canonical Forms [1]
Replace ∑ with ∏ (or vice versa) and replace those j’s that appeared in the original form with those that do not.
Example: f1(a,b,c) = a’b’c + a’bc’ + ab’c’ + abc’ = m1 + m2 + m4 + m6 = ∑m(1,2,4,6) = ∏M(0,3,5,7)
= ∏M(000,011,101,111) = (a+b+c)•(a+b’+c’)•(a’+b+c’)•(a’+b’+c’)
F2(x,y, z) = (x+y’+z).(x+y+z’)
= ∏M(010, 001) = ∏M(1,2)
=∑m(0,3,4,5,6, 7)
= x’y’z’ + x’yz+xy’z’+xy’z+xyz’+xyz

## Slide 25: Implementation of SOP Expressions[1]
Sum-of-Products expressions can be implemented using:
  2-level AND-OR logic circuits
  2-level NAND logic circuits
AND-OR logic circuit
F = AB + CD + E
F
A
B
D
C
E
F’’ = F = (AB + CD + E)’’
= ((AB)’.(CD)’(E)’)’

## Slide 26: Implementation of SOP Expressions contd.
NAND-NAND circuit (by circuit transformation)
a) add double bubbles
b) change OR-with-
inverted-inputs to NAND
& bubbles at inputs to
their complements
F
A
B
D
C
E
A
B
D
C
E'
F
F’’ = F = (AB + CD + E)’’
= ((AB)’.(CD)’(E)’)’
F’’ = F = (AB + CD + E)’’
= ((AB)’.(CD)’(E)’)’
Y = (AB)’ = A’+B’

## Slide 27: Implementation of POS Expressions[1]
Product-of-Sums expressions can be implemented using:
  2-level OR-AND logic circuits
  2-level NOR logic circuits
OR-AND logic circuit
G = (A+B).(C+D).E
G
A
B
D
C
E

## Slide 28: Implementation of POS Expressions contd.
NOR-NOR circuit (by circuit transformation):
a) add double bubbles
b) changed AND-with-
inverted-inputs to NOR
& bubbles at inputs to
their complements
G
A
B
D
C
E
A
B
D
C
E'
G

## Slide 29: References
[1] M. Morris Mano and Michael D. Ciletti, “Digital Design with an Introduction to the Verilog HDL,” 5th Edition, Pearson Education,2013.
[2] Reshu Gupta, Amit Gupta ,Atul Kumar Sharma “ Switching Theory(Digital Electronics)”, Tech India Publication Series, Satya Prakashan, New Delhi.
[3] R. P. Jain, “Modern Digital Electronics,” 4th Edition, Tata McGraw-Hill Education, 2009.