## Slide 1: Digital Systems 18B11EC213
Signal and Its Classifications

## Slide 2: Contents
Signal Definition
CT and DT Signals
Even and Odd
Periodicity
Energy and Power
Basic CT and DT signals
Signal Transformation

## Slide 3: Signal
A signal is a function of one or more independent variables and typically it contains information about the behavior or nature of the phenomenon.
Mathematically, a signal is represented as a function of an independent variable t. Usually t represents time. Thus, a signal is denoted by x(t).

## Slide 4: Continuous-Time and Discrete-Time Signals
A signal x(t) is a continuous-time signal if t is a continuous variable.
If t is a discrete variable-that is, x(t) is defined at discrete times-then x(t) is a discrete-time signal.
Since a discrete-time signal is defined at discrete times, a discrete-time signal is often identified as a sequence of numbers, denoted by {xn} or x[n], where n = integer. Illustrations of a continuous-time signal x(t) and of a discrete-time signal x[n] are shown in Fig. 1.

## Slide 5
Fig. 1 Graphical representation of (a) continuous-time and (b) discrete-time signals
(a)
(b)

## Slide 6: Even and Odd Signals
A signal x(t) or x[n] is called to be an even signal if
x(-t) = x(t)
x[-n] = x[n]
The even signals have symmetry about vertical axis.
A signal x(t) or x[n] is said to be an odd signal if
x(-t) = -x(t)
x[-n] = -x[n]
The odd signals have anti-symmetry about vertical axis.

## Slide 7: Examples of even and odd signals
Fig. 2. Examples of even signals (a and b) and odd signals (c and d).

## Slide 8: Even and Odd Parts
Any signal x(t) or x[n] can be expressed as a sum of two signals, one of which is even and one of which is odd. That is,
x(t) = xe(t) + x0(t)
x[n] = xe[n] + x0[n]

## Slide 9: Even and Odd Parts
Ex. Find the even and odd components of x(t) = ejt
Sol: x(t) = ejt = xe(t) + x0(t)

## Slide 10: Even and Odd Parts
Ex. Sketch and label the even and odd components of the following signals:
(a) (b)
(c)

## Slide 11: Even and Odd Parts
Sol. (a)
Sol. (b)

## Slide 12: Even and Odd Parts
Sol. (c)

## Slide 13: Periodic and Non-periodic Signals
A continuous-time signal x(t) is said to be periodic with period T if there is a positive nonzero value of T for which
x(t + T) = x(t) for all t
The fundamental period T0 of x(t) is the smallest positive value of T for which above Eq. holds.
Note that this definition does not work for a constant signal x(t) (known as a dc signal). For a constant signal x(t) the fundamental period is undefined since x(t) is periodic for any choice of T (and so there is no smallest positive value).
Any continuous-time signal which is not periodic is called a non-periodic (or aperiodic) signal.

## Slide 14: Examples of Periodic Signals
Fig. 3. Examples of periodic signals (a) continuous time periodic signal (b) discrete time periodic signal

## Slide 15: Periodic discrete-time signals
A sequence (discrete-time signal) x[n] is periodic with period N if there is a positive integer N for which
x[n + N] = x[n] for all n
The fundamental period N0 of x[n] is the smallest positive integer N for which above Eq. holds.
Any sequence which is not periodic is called a non-periodic (or aperiodic) sequence.
Note that a sequence obtained by uniform sampling of a periodic continuous-time signal may not be periodic.
Note also that the sum of two continuous-time periodic signals may not be periodic but that the sum of two periodic discrete sequences is always periodic.

## Slide 16
In other words, the sum of two periodic signals is periodic only if the ratio of their respective periods can be expressed as a rational number.
Then the fundamental period is the least common multiple of T1 and T2. If the ratio T1/T2 is an irrational number, then the signals x1(t) and x2(t) do not have a common period and x(t) cannot be periodic.
Ex. Let x1(t) and x2(t) be periodic signals with fundamental periods T1 and T2, respectively. Under what conditions is the sum x(t) = x1(t) + x2(t) periodic, and what is the fundamental period of x(t) if it is periodic?
Sol.
Periodicity

## Slide 17
Ex. Let x1[n] and x2[n] be periodic sequences with fundamental periods N1 and N2, respectively. Under what conditions is the sum x[n] = x1[n] + x2[n] periodic, and what is the fundamental period of x[n] if it is periodic?
Sol. The sum of two periodic sequences is also periodic and its fundamental period is the least common multiple of N1 and N2.
Periodicity

## Slide 18: Periodicity
Ex. Check the periodicity of the following signals:
(a)
(b)
Sol: (a) The signal is always periodic with fundamental period T0 given as
(b) The signal is periodic only if

## Slide 19: Periodicity
Ex. Let x(t) is a complex exponential signal
If x[n] is obtained by uniform sampling of x(t) with sampling interval Ts, that is
Find the condition on Ts so that x[n] is periodic.
Sol: (a) The signal, x[n] is periodic if ratio of Ts/T0 is rational that is

## Slide 20: Periodicity
Ex. Consider the sinusoidal signal x(t) = cos15t
(a) Find the value of Ts such that x[n] = x(nTs) is a periodic sequence.
(b) Find the fundamental period of x[n] if Ts = 0.1π
Sol: (a) The signal, x[n] is periodic if ratio of Ts/T0 is rational that is
(b) The fundamental period of x[n] is calculated as follows.
and
The smallest positive integer N is obtained for m = 3. Thus, fundamental period of x[n] is N = 4 samples.

## Slide 21: Periodicity
Ex. Determine whether or not the following signals are periodic. If periodic then find the fundamental period also.
(a) x(t) = cos(π/3)t + sin(π/4)t
(b) x(t) = cost + sin√2t
(c) x[n] = exp(jπn/4)
(d) x[n] = cos(π/3)n + sin(π/4)n
Sol: (a) T1 = 6, T2 = 8, T1/T2 = ¾ = rational, hence periodic.
Fundamental period T = LCM of T1 and T2 = 24
(b) T1 = 2π, T2 = √2π, T1/T2 = √2 = not a rational number, hence aperiodic.
(c) ω0/2π = 1/8 = rational, hence periodic.
Fundamental period, N = 8 samples
(d) N1 = 6, N2 = 8, Both signals are periodic, hence their sum is also periodic.
Fundamental period, N = LCM of N1 and N2 = 24 samples

## Slide 22: Energy and Power Signals
For an arbitrary continuous-time signal x(t), the normalized energy content E of x(t) is defined as
The normalized average power P of x(t) is defined as

## Slide 23: Energy and Power Signals
Similarly, for a discrete-time signal x[n], the normalized energy content E of x[n] is defined as
The normalized average power P of x[n] is defined as

## Slide 24: Energy and Power Signals
x(t) (or x[n]) is said to be an energy signal (or sequence) if and only if 0 < E < ∞, and so P = 0.
x(t) (or x[n]) is said to be a power signal (or sequence) if and only if 0 < P < ∞, thus implying that E = ∞.
Signals that satisfy neither property are referred to as neither energy signals nor power signals.
Note that a periodic signal is a power signal if its energy content per period is finite, and then the average power of this signal need only be calculated over a period.

## Slide 25: Energy and Power Signals
Ex. Determine whether the following signals are energy signals, power signals or neither.
x(t) = e-atu(t), a > 0
x(t) = tu(t)
x[n] = u[n]
x[n] = 2ej3n
x[n] = (-0.5)nu[n]
Sol: (a) E = 1/2a, energy signal
(b) E = inf, P = inf, neither energy nor power
(c) P = ½, power signal
(d) P = 4, power signal
(e) E = 4/3, energy signal

## Slide 26: Basic Continuous-Time and Discrete-Time Signals
A. The Unit Step Function The unit step function u(t), also known as the Heaviside unit function, is defined as
The unit step sequence u[n], is defined as
u[n]
1
0
n
1
2
X(t) = u(t)
1
0
t

## Slide 27: Basic Continuous-Time and Discrete-Time Signals
B. The Unit Impulse Function
The unit impulse function δ(t), also known as the Dirac delta function, is defined as
The unit impulse (or unit sample) sequence δ[n] is defined as

## Slide 28: Basic Continuous-Time and Discrete-Time Signals
C. The Unit Ramp Function
The unit ramp function r(t), is defined as
The unit ramp sequence r[n], is defined as
r(t)
1
0
t
1
r[n]

## Slide 29: Signal Transformation and Properties
The original signal x(t) is shifted by an amount tₒ that is x(t ± tₒ).
Time Shifting
Time Scaling
The original signal x(t) is scaled by an amount a that is x(at).
a>1 Period reduces and graph shrink or compress
a<1 Period increases and graph Expands

## Slide 30: Signal Transformation and Properties
The original signal x(t) is reversed in time that is x(-t).
Time Reversal

## Slide 31: Signal Transformation
Ex. A continuous-time signal x(t) is shown below. Sketch and label each of the following signals.
(a) x(t- 2); Time Shifting
(b) x(2t); Time Scaling
(c) x(t/2); Time Scaling
(d) x(-t) Time Reversal

## Slide 32
Sol:
(a) x(t- 2); Time Shifting
(b) x(2t); Time Scaling (time compression)
(c) x(t/2); Time Scaling (time expansion)
(d) x(-t) Time Reversal

## Slide 33: Reference
Signals-and-systems-2nd-edition-schaums-outline-series-hwei-hsu