## Slide 1: ASSEMBLY LANGUAGE PROGRAMMING
JIIT-128, Noida

## Slide 2: Programming
JIIT-128, Noida
87
1. Write an assembly program to add two numbers
  MVI D, 02BH
  MVI C, 06FH
  MOV A, C
  ADD D
  STA 4500
  HLT

## Slide 3: Program
JIIT-128, Noida
88
Write an assembly program to add two numbers
  LXI H, 4500
  MOV A, M
  INX H
  ADD M
  STA 4500
  HLT

## Slide 4: Program
JIIT-128, Noida
89
2. Write an Assembly Language Program to add two numbers ;
results contain carry
LXI H, 4500 MOV A, M INX H
ADD M
JNC LOOP 1 INR C
STA 4500
MOV A, C STA 4501 HLT
LOOP1

## Slide 5: Program
JIIT-128, Noida
90
2. Write an Assembly Language Program to add two numbers ; results contain carry ( write the program using JC)
LXI H, 4500 MOV A, M INX H
ADD M
 | JC | LOOP 1
 | JMP | LOOP 2
LOOP1 | INR C | 
STA 4500 MOV A, C STA 4501 HLT
LOOP1

## Slide 6: ADDITION OF TWO 16 – BIT NUMBERS
91
3. To write an assembly language program for adding two 16
bit numbers using 8085 micro processor.
JIIT-128, Noida

## Slide 7: SUM OF DATAS
92
4. To write an assembly language program to
calculate the sum of datas using 8085 microprocessor
JIIT-128, Noida

## Slide 8: SUBTRACTION OF TWO 8 BIT NUMBERS
93
5. To write a assembly language program for subtracting 2 bit
(8) numbers by using- 8085
JIIT-128, Noida

## Slide 9: SUBTRACTION OF TWO 16 BIT NUMBERS
94
6. To write an assembly language program for subtracting two
16 bit numbers using 8085 microprocessor kit.
JIIT-128, Noida

## Slide 10: Multiplication ; No carry
JIIT-128, Noida
95
LDA 2000 // Load multiplicant to accumulator
MOV B,A // Move multiplicant from A(acc) to B register
LDA 2001 // Load multiplier to accumulator
MOV C,A // Move multiplier from A to C
MVI A,00 // Load immediate value 00 to a
L: ADD B // Add B(multiplier) with A
DCR C // Decrement C, it act as a counter
JNZ L // Jump to L if C reaches 0
STA 2010 // Store result in to memory
HLT // End

## Slide 11: Multiplication ; With carry
JIIT-128, Noida
96
7. Write an assembly program to multiply a number by 8
MVI C,OO LXI H, 4100 MOV B, M INX H MOV A, M DCR B
LOOP 2 ADD M
JNC
INR C LOOP 1 DCR B
JNZ
LOOP1
LOOP2
STA 4500
HLT

## Slide 12: Multiplication
JIIT-128, Noida
97

## Slide 13: DIVISION OF TWO 8 – BIT NUMBERS
98
To write an assembly language program for
dividing two 8 bit numbers using microprocessor
JIIT-128, Noida

## Slide 14: ASCENDING ORDER
99
9. To write a program to sort given ‘n’ numbers in
ascending order
JIIT-128, Noida

## Slide 15: DESCENDING ORDER
100
10. To write a program to sort given ‘n’ numbers
in descending order
JIIT-128, Noida

## Slide 16: Largest Number
JIIT-128, Noida
101
Write an Assembly Language Program to find a largest number.
LXI H, 4500 MOV A, M INX H CMP M
JNC JMP
LOOP 1
LOOP 2
LOOP1 LOOP2
STA 4500 MOV A, M STA 4500 HLT

## Slide 17: Smallest Number
JIIT-128, Noida
102
Write an Assembly Language Program to find a smallest number.
LXI H, 4500 MOV A, M INX H CMP M
JC LOOP 1
JMP LOOP 2
LOOP1 LOOP2
STA 4500 MOV A, M STA 4500 HLT

## Slide 18: References
Gaonkar, R. S. (1990). Microprocessor Architecture, Programming and Applications with the 8085. Fifth Edition Prentice Hall PTR.