## Slide 1: Module 6

## Slide 2: Contents
Addressing Modes
Types and sizes of operands
Types of Instruction

## Slide 3: Addressing Modes [1]
A machine instruction can find its operand in one of three places:
As a part of the instruction (Immediate addressing mode)
In a general-purpose register
In memory
Addressing modes refers to the way in which the operand of an instruction is specified.
Consequently, addressing modes can be broadly classified into:
direct – the address field specifies the operand address and
indirect– the address field specifies a location that contains the operand address.

## Slide 4: Immediate Addressing Mode
Operand is a constant encoded in the instruction itself
Add R4, #3 /* R4 <- R4 + 3
No memory reference to fetch data
Fast, but Limited range
Used to define and use constants or set initial values of variables
Disadvantage:
Size of the operand is limited to the size of address field of instruction. In most instruction set address field of operand is small compared to instruction size.

## Slide 5: Immediate Addressing Mode
Operand is a constant encoded in the instruction itself
Add R4, #3 /* R4 <- R4 + 3
Operand value
Instruction
Immediate mode

## Slide 6: Direct Addressing Mode
  Direct (Absolute): Address is a constant ,encoded in the instruction
  Add R1,(1001) /* R1 =R1 + M[1001]
  + Single memory reference to access data
  + No additional calculations to work out effective address
  - Limited address space
  Use: accessing static data

## Slide 7: Direct Addressing Mode
  Direct (Absolute): Address is a constant ,encoded in the instruction
  Add R1,(1001) /* R1 =R1 + M[1001]
1000
Instruction
Direct mode
1000
Operand
Memory

## Slide 8: Indirect Addressing Mode
  Why Indirect addressing?
      In direct addressing length of address field of operand is less than the word size, so it provides limited address space.
      Using indirect addressing mode, full-length address of operand can be used.
Indirect : effective address is in the memory, and corresponding memory address will be maintained in the address field of an instruction.
  Add R1,@1001 /* R1 =R1 + M[[1001]]
  +
  +

## Slide 9: Indirect Addressing Mode
  +
  +
1000
Instruction
Indirect mode
1000
3000
Memory
3000
Operand
Two memory reference to access data
For word length N, available address space is 2^N
The number of different effective addresses that may be referenced at any one time is limited to 2^K, where K is the length of the address field

## Slide 10: Register Addressing Mode
  Register Mode: Operand is held in register named in the address filed of the instruction
Add R4,R3 /* R4=R4+R3
If content of address field of instruction is 6 then register R6 is the intended address, and the operand value is contained in R5
Generally, 3 to 5 bits is used in address field, so only 8 to 32 register can be referenced.

## Slide 11: Register Addressing Mode
Small address field is needed in instruction
110
Instruction
Register direct mode
R6
Operand
GPRs
R5
R3
No memory reference
Limited address space

## Slide 12: Register Indirect Addressing Mode
Add R4,(R1) /* R4=R4+M[R1]
Register Indirect Mode: As register addressing is similar to direct addressing, register indirect addressing is similar to indirect addressing
+ Large address space
- Multiple memory accesses to find operand, Hence slower
Use: accessing a pointer or computed address

## Slide 13: Register Indirect Addressing Mode
110
Instruction
Register indirect mode
R6
3000
GPRs
R5
R3
Operand
Memory
3000

## Slide 14: Register Indirect Addressing Mode
The advantages and limitations of register indirect addressing are basically the same as for indirect addressing.
In both cases, the address space limitation (limited range of addresses) of the address field is overcome by having that field refer to a word- length location containing an address. In addition, register indirect addressing uses one less memory reference than indirect addressing[4].

## Slide 15
Displacement Addressing
Relative addressing
Base-register addressing
Indexing
Combines the capabilities of direct addressing and register indirect addressing

## Slide 16: Relative Addressing
Content of the program counter is added to the address part of the instruction in order to obtain the effective address.
Effective address= PC + Address field value
110
Operand
Memory
Opcode
PC
+

## Slide 17: Base-Register Addressing
Content of a base register is added to the address part of the instruction to obtain the effective address.
EA= Base register + Address field value. Load R1 20(R2) then EA=20+[R2] , R2 is base register
Address
R6
GPRs
Operand
Memory
3000
17
Base Register
+

## Slide 18
It is use to implement segmentation.
The base register holds the base address of segment and address field of instruction holds displacement.
Address field size= K
No of possible register = N
Then one instruction can reference any one of N areas of 2K words.
Base-Register Addressing

## Slide 19: Index-Register Addressing
Content of a index register is added to the address part of the instruction to obtain the effective address.
EA= index register + Address field value. Load R1 20(R2) then EA= 20+[R2], R2 is index register
Address
R6
GPRs
Operand
Memory
3000
19
index Register
+

## Slide 20
The address field references a main memory address, and the referenced register contains a positive displacement from that address.
Consider, for example, a list of numbers stored starting at location A.
Suppose that we would like to add 1 to each element on the list. We need to fetch each value, add 1 to it, and store it back
The sequence of effective addresses that we need is A, A + 1, A + 2, . . . , up to the last location on the list.
With indexing, this is easily done. The value A is stored in the instruction’s address
field, and the chosen register, called an index register, is initialized to 0. After each
operation, the index register is incremented by 1.
Index-Register Addressing

## Slide 21: Auto Indexed (increment mode):
Effective address of the operand is the contents of a register specified in the instruction. After accessing the operand, the contents of this register are automatically incremented to point to the next consecutive memory location.(R1)+. Here one register reference, one memory reference and one ALU operation is required to access the data.
Example: Add R1, (R2)+ // OR
R1 = R1 +M[R2]
R2 = R2 + d
Useful for stepping through arrays in a loop. R2 – start of array d – size of an element

## Slide 22
22
Rauto
x
Memory
3000
Auto increment register
3000
R1
Before Execution
After Execution
22
Rauto
x
3000
3001
X
R1
3001
y

## Slide 23: Auto Indexed (decrement mode):
Effective address of the operand is the contents of a register specified in the instruction. Before accessing the operand, the contents of this register are automatically decremented to point to the previous consecutive memory location. –(R1) Here one register reference, one memory reference and one ALU operation is required to access the data.
Example:
Add R1,-(R2) //OR
R2 = R2-d
R1 = R1 + M[R2]

## Slide 24
24
24
Rauto
x
Memory
3000
Auto increment register
3000
R1
Before Execution
After Execution
24
Rauto
x
2999
2999
p
R1
3001
y
p
3000

## Slide 25
The stack is a reserved block of locations. Items are appended to the top of the stack so that, at any given time, the block is partially filled.
Associated with the stack is a pointer whose value is the address of the
top of the stack.
Alternatively, the top two elements of the stack may be in processor registers, in which case the stack pointer references the third element of the stack.
The stack pointer is maintained in a register. Thus, references to stack locations in
memory are in fact register indirect addresses.
Stack Addressing

## Slide 26: Summarizing All Addressing Modes
Addressing Mode | Example Instruction | Meaning | When Used
Register | Add R4, R3 | R4  R4 + R3 | When a value is in a register
Immediate | Add R4, #3 | R4  R4 + 3 | For constants
Displacement | Add R4, 100(R1) | R4  R4 + Mem[100+R1] | Accessing local variables
Register deferred or Indirect | Add R4, (R1) | R4  R4 + Mem[R1] | Accessing using pointer or computed address
Indexed | Add R3, (R1+R2) | R3  R3 + Mem[R1+R2] | Array addressing; R1 = base of array, R2 = index amount
Direct or Absolute | Add R1, (1001) | R1  R1 + Mem[1001] | Accessing static data; addr. constant may need to be big
Notes: When might some of these be used – give an example…

## Slide 27: Summarizing All Addressing Modes
Addressing Mode | Example Instruction | Meaning | When Used
Memory indirect or Memory deferred | Add R1, @(R3) | R1  R1 + Mem[Mem[R3] | If R3 is the address of a pointer p, then mode yields *p
Autoincrement | Add R1, (R2)+ | R1  R1+Mem[R2]; R2  R2 + d | Useful for stepping through arrays within a loop; R2 points to start of array; each ref. increments R2 by d
Autodecrement | Add R1, -(R2) | R1  R1-Mem[R2]; R2  R2 + d | Same as autoincrement; can be used for push/pop on stack
Scaled | Add R1, 100(R2), [R3] | R1  R1 + Mem[100+R2+R3*d] | Used to index arrays

## Slide 28: Example
PC: Program counter
R1: Register
XR: Indexed register
AC: Accumulator
Fig.1 [1]

## Slide 29
Fig.2 [1]

## Slide 30
Fig.3 [1]

## Slide 31: Types and sizes of operands
How is the type of an operand designated?
  – Encoded in the opcode
  – Annotated by tags
Common operand types:
  Character - 8bits
  Half word - 16 bits, 2 bytes
  Word - 32 bits, 4 bytes
  Single precision floating point - 32 bits, 4 bytes
  Double precision floating point - 64 bits, 8 bytes
Most instructions have three operands (z = x + y)
Well-known ISAs specify 0-3 (explicit) operands per instruction
Operands can be specified implicitly or explicitly (see previous slides of classifying ISA)

## Slide 32: Types and sizes of operands
Encoding of characters:
  – ASCII
  – UNICODE
Encoding of integers(signed):
  – Two’s complement binary numbers
  http://en.wikipedia.org/wiki/Two's_complement
Encoding of floating point numbers:
  – IEEE standard 754

## Slide 33: Expanding Opcodes [2]
We have seen that how the number of operands in an instruction is dependent on the instruction length; we must have enough bits for the opcode and for the operand addresses
However, not all instructions require the same number of operands
Expanding opcodes represent a compromise between the need for a rich set of opcodes and the desire to have short opcodes, and thus short instructions.
The idea is to make some opcodes short, but have a means to provide longer ones when needed.
  When the opcode is short, a lot of bits are left to hold operands (which mean we could have two or three operands per instruction).

## Slide 34: Expanding Opcodes
When we don’t need any space for operands (for an instruction such as Halt or because the machine uses a stack), all the bits can be used for the opcode, which allows for many unique instructions
  In between, there are longer opcodes with fewer operands as well as shorter opcodes with more operands
Consider a machine with 16-bit instructions and 16 registers. Because we now have a register set instead of one simple accumulator, we need to use 4 bits to specify a unique register. We could encode 16 instructions, each with 3 register operands (which implies any data to be operated on must first be loaded into a register).
Or,
Use 4 bits for the opcode and 12 bits for a memory address (assuming a memory of size 4K). However, if all data in memory is first loaded into a register in this register set, the instruction can select that particular data element using only 4 bits (assuming 16 registers).
These two choices are illustrated in the following figure:

## Slide 35: Example
Opcode Address 1 Address 2 Address 3
Opcode Address
Fig. Two Possibilities for a 16-Bit Instruction Format

## Slide 36: But why limit the opcode to only 4 bits?
If we allow the length of the opcode to vary, that changes the number of remaining bits that can be used for operand addresses.
Using expanding opcodes, we could allow for opcodes of 8 bits that require two register operands; or we could allow opcodes of 12 bits that operate on one register; or we could allow for 16-bit opcodes that require no operands.
Three More Possibilities for a 16-Bit Instruction Format

## Slide 37
Consider a machine in which instructions are 16 bits long and addresses are 4 bits long.
• This might be reasonable on a machine that has 16 registers on which all arithmetic operations take place.
• One design would be a 4-bit opcode and three addresses in each instruction, giving 16 three address instructions.[5]
Opcode Address 1 Address 2 Address 3

## Slide 38
However, if the designers need 15 three-address instructions, 14 two-address instructions, 31 one-address instructions, and 16 instructions with no address at all, they can use opcodes 0 to 14 as three-address instructions but interpret opcode 15 differently.
Fig.a [5]

## Slide 39: Escape Opcode
The only issue is that we need a method to determine when the instructions should be interpreted as having a 4-bit, 8-bit, 12-bit, or 16-bit opcode
The trick is to use an “escape opcode” to indicate which format should be used
While allowing for a wider variety of instructions, this expanding opcode scheme also makes the decoding more complex. Instead of simply looking at a bit pattern and deciding which instruction it is, we need to decode the instruction something like this:
if (leftmost four bits != 1111 ) {
Execute appropriate three-address instruction}
else if (leftmost seven bits != 1111 111 ) {
Execute appropriate two-address instruction}
else if (leftmost twelve bits != 1111 1111 1111 ) {
Execute appropriate one-address instruction }
else {
Execute appropriate zero-address instruction
}

## Slide 40: Escape Opcode
At each stage, one spare code—the escape code—is used to indicate that we should now look at more bits
This is another example of the types of trade-offs hardware designers continually face:
Here, we trade opcode space for operand space.
Example: Given 8-bit instructions, it is possible to use expanding opcodes to allow the following to be encoded? If so, show the encoding.
• 3 instructions with two 3-bit operands
• 2 instructions with one 4-bit operand
• 4 instructions with one 3-bit operand

## Slide 41: Example
First, we must determine if the encoding is possible:
3 * 23 * 23 = 3 * 26 = 192
2 * 24 = 32
4 * 23 = 32
If we sum the required number of bit patterns, we get 192 + 32 + 32 = 256. 8 bits in the instruction means a total of 28 = 256 bit patterns, so we have an exact match (which means the encoding is possible, but every bit pattern will be used in creating it).
The encoding we can use is as follows:
00 xxx xxx
01 xxx xxx 3 instructions with two 3-bit operands
10 xxx xxx
11 – Escape opcode
1100 xxxx
1101 xxxx 2 instructions with one 4-bit operand
1110 – Escape opcode
1111 – Escape opcode
11100 xxx
11101 xxx 4 instructions with one 3-bit operand
11110 xxx
11111 xxx

## Slide 42: Types of Instruction [3]
Depending on operation they perform, all instructions are divided in several groups:
Arithmetic Instructions
Data Transfer Instructions
Logic Instructions
Bit-oriented Instructions
Branch Instructions

## Slide 43: MNEMONICS and OPERAND
The first part of each instruction, called MNEMONIC refers to the operation an instruction performs (copy, addition, logic operation etc.).
Mnemonics are abbreviations of the name of operation being executed.
For example:
  INC R1: Increment register R1 (increment register R1);
  JNZ LOOP: Jump if Not Zero LOOP (if the value in the accumulator is not 0, jump to the address marked as LOOP);
The other part of instruction, called OPERAND (separated from mnemonic by at least one whitespace) defines data being processed by instructions.
Some of the instructions have no operand, while some of them have one, two or three. If there is more than one operand in an instruction, they are separated by a comma. For example:

## Slide 44: MNEMONICS and OPERAND
Some of the instructions have no operand, while some of them have one, two or three.
If there is more than one operand in an instruction, they are separated by a comma. For example:
RET - return from a subroutine;
JZ TEMP - if the number in the accumulator is not 0, jump to the address marked as TEMP;
ADD A,R3 - add R3 and accumulator;
CJNE A,#20,LOOP - compare accumulator with 20. If they are not equal, jump to the address marked as LOOP;

## Slide 45: Arithmetic Instructions
Arithmetic instructions perform several basic operations such as addition, subtraction, division, multiplication etc.
After execution, the result is stored in the first operand.
For example:
ADD A,R1 - The result of addition (A+R1) will be stored in the accumulator.

## Slide 46: Arithmetic Instructions
Mnemonic | Description | Byte | Cycle
ADD A,Rn | Adds the register to the accumulator | 1 | 1
ADD A,direct | Adds the direct byte to the accumulator | 2 | 2
DD A,@Ri | Adds the indirect RAM to the accumulator | 1 | 2
ADD A,#data | Adds the immediate data to the accumulator | 2 | 2
ADDC A,Rn | Adds the register to the accumulator with a carry flag | 1 | 1
ADDC A,direct | Adds the direct byte to the accumulator with a carry flag | 2 | 2
ADDC A,@Ri | Adds the indirect RAM to the accumulator with a carry flag | 1 | 2
ADDC A,#data | Adds the immediate data to the accumulator with a carry flag | 2 | 2
SUBB A,Rn | Subtracts the register from the accumulator with a borrow | 1 | 1

## Slide 47: Data Transfer Instructions
Data transfer instructions move the content of one register to another.
The register the content of which is moved remains unchanged.
If they have the suffix “X” (MOVX), the data is exchanged with external memory.
Mnemonic | Description | Byte | Cycle
MOV A,Rn | Moves the register to the accumulator | 1 | 1
MOV A,direct | Moves the direct byte to the accumulator | 2 | 2
MOV A,@Ri | Moves the indirect RAM to the accumulator | 1 | 2
MOV A,#data | Moves the immediate data to the accumulator | 2 | 2
MOV Rn,A | Moves the accumulator to the register | 1 | 2

## Slide 48: Data Transfer Instructions
Mnemonic | Description | Byte | Cycle
MOV A,Rn | Moves the register to the accumulator | 1 | 1
MOV A,direct | Moves the direct byte to the accumulator | 2 | 2
MOV A,@Ri | Moves the indirect RAM to the accumulator | 1 | 2
MOV A,#data | Moves the immediate data to the accumulator | 2 | 2
MOV Rn,A | Moves the accumulator to the register | 1 | 2
MOV Rn,direct | Moves the direct byte to the register | 2 | 4
MOV Rn,#data | Moves the immediate data to the register | 2 | 2
MOV direct,A | Moves the accumulator to the direct byte | 2 | 3
MOV direct,Rn | Moves the register to the direct byte | 2 | 3
MOV direct,direct | Moves the direct byte to the direct byte | 3 | 4
MOV direct,@Ri | Moves the indirect RAM to the direct byte | 2 | 4

## Slide 49: Data Transfer Instructions
Mnemonic | Description | Byte | Cycle
MOV direct,#data | Moves the immediate data to the direct byte | 3 | 3
MOV @Ri,A | Moves the accumulator to the indirect RAM | 1 | 3
MOV @Ri,direct | Moves the direct byte to the indirect RAM | 2 | 5
MOV @Ri,#data | Moves the immediate data to the indirect RAM | 2 | 3
MOVC A,@A+PC | Moves the code byte relative to the PC to the accumulator (address=A+PC) | 1 | 3
MOVX A,@Ri | Moves the external RAM (8-bit address) to the accumulator | 1 | 3-10
MOVX @Ri,A | Moves the accumulator to the external RAM (8-bit address) | 1 | 4-11
PUSH direct | Pushes the direct byte onto the stack | 2 | 4
POP direct | Pops the direct byte from the stack/td> | 2 | 3

## Slide 50: Data Transfer Instructions
Mnemonic | Description | Byte | Cycle
XCH A,Rn | Exchanges the register with the accumulator | 1 | 2
XCH A,direct | Exchanges the direct byte with the accumulator | 2 | 3
XCH A,@Ri | Exchanges the indirect RAM with the accumulator | 1 | 3
XCHD A,@Ri | Exchanges the low-order nibble indirect RAM with the accumulator | 1 | 3

## Slide 51: Logic Instructions
Logic instructions perform logic operations upon corresponding bits of two registers.
After execution, the result is stored in the first operand.
Mnemonic | Description | Byte | Cycle
ANL A,Rn | AND register to accumulator | 1 | 1
ANL A,direct | AND direct byte to accumulator | 2 | 2
ANL A,@Ri | AND indirect RAM to accumulator | 1 | 2
ANL A,#data | AND immediate data to accumulator | 2 | 2
ANL direct,A | AND accumulator to direct byte | 2 | 3
ANL direct,#data | AND immediae data to direct register | 3 | 4

## Slide 52: Logic Instructions
Mnemonic | Description | Byte | Cycle
ORL A,Rn | OR register to accumulator | 1 | 1
ORL A,direct | OR direct byte to accumulator | 2 | 2
ORL A,@Ri | OR indirect RAM to accumulator | 1 | 2
ORL direct,A | OR accumulator to direct byte | 2 | 3
ORL direct,#data | OR immediate data to direct byte | 3 | 4
XRL A,Rn | Exclusive OR register to accumulator | 1 | 1
XRL A,direct | Exclusive OR direct byte to accumulator | 2 | 2
XRL A,@Ri | Exclusive OR indirect RAM to accumulator | 1 | 2
XRL A,#data | Exclusive OR immediate data to accumulator | 2 | 2
XRL direct,A | Exclusive OR accumulator to direct byte | 2 | 3
XORL direct,#data | Exclusive OR immediate data to direct byte | 3 | 4

## Slide 53: Logic Instructions
Mnemonic | Description | Byte | Cycle
CLR A | Clears the accumulator | 1 | 1
CPL A | Complements the accumulator (1=0, 0=1) | 1 | 1
SWAP A | Swaps nibbles within the accumulator | 1 | 1
RL A | Rotates bits in the accumulator left | 1 | 1
RLC A | Rotates bits in the accumulator left through carry | 1 | 1
RR A | Rotates bits in the accumulator right | 1 | 1
RRC A | Rotates bits in the accumulator right through carry | 1 | 1

## Slide 54: Bit-oriented Instructions
Similar to logic instructions, bit-oriented instructions perform logic operations.
The difference is that these are performed upon single bits.
Mnemonic | Description | Byte | Cycle
CLR C | Clears the carry flag | 1 | 1
CLR bit | Clears the direct bit | 2 | 3
SETB C | Sets the carry flag | 1 | 1
SETB bit | Sets the direct bit | 2 | 3
CPL C | Complements the carry flag | 1 | 1
CPL bit | Complements the direct bit | 2 | 3
ANL C,bit | AND direct bit to the carry flag | 2 | 2

## Slide 55: Bit-oriented Instructions
Mnemonic | Description | Byte | Cycle
ANL C,/bit | AND complements of direct bit to the carry flag | 2 | 2
ORL C,bit | OR direct bit to the carry flag | 2 | 2
ORL C,/bit | OR complements of direct bit to the carry flag | 2 | 2
MOV C,bit | Moves the direct bit to the carry flag | 2 | 2
MOV bit,C | Moves the carry flag to the direct bit | 2 | 3

## Slide 56: Branch Instructions
There are two kinds of branch instructions:
Unconditional jump instructions: upon their execution a jump to a new location from where the program continues execution is executed.
Conditional jump instructions: a jump to a new program location is executed only if a specified condition is met. Otherwise, the program normally proceeds with the next instruction.
Mnemonic | Description | Byte | Cycle
ACALL addr11 | Absolute subroutine call | 2 | 6
LCALL addr16 | Long subroutine call | 3 | 6
RET | Returns from subroutine | 1 | 4
RETI | Returns from interrupt subroutine | 1 | 4
AJMP addr11 | Absolute jump | 2 | 3

## Slide 57: Branch Instructions
Mnemonic | Description | Byte | Cycle
LJMP addr16 | Long jump | 3 | 4
SJMP rel | Short jump (from –128 to +127 locations relative to the following instruction) | 2 | 3
JC rel | Jump if carry flag is set. Short jump. | 2 | 3
JNC rel | Jump if carry flag is not set. Short jump. | 2 | 3
JB bit,rel | Jump if direct bit is set. Short jump. | 3 | 4
JBC bit,rel | Jump if direct bit is set and clears bit. Short jump. | 3 | 4
JMP @A+DPTR | Jump indirect relative to the DPTR | 1 | 2
JZ rel | Jump if the accumulator is zero. Short jump. | 2 | 3
JNZ rel | Jump if the accumulator is not zero. Short jump. | 2 | 3
NOP | No operation | 1 | 1

## Slide 58: References
M. Morris Mano, Computer System Architecture, Prentice Hall of India Pvt Ltd, 3rd Edition (updated) , 30 June 2017
the Essentials of Computer Organization and Architecture (4th Edition), Linda Null and Julia Lobur, Jones and Barlett Publishers, ISBN: 978-1-284-07448-2.
Barry B. Brey, The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486, Pentium, Pentium Pro Processor, Pentium II, Pentium III, Pentium 4, and Core2 with 64-bit Extensions : Architecture, Programming, and Interfacing. Pearson Education India, Eigth Edition, 2019
4. Computer Organization and Architecture Designing for Performance Tenth Edition William Stallings
5.http://www.personal.kent.edu/~aguercio/CS35101Slides/Tanenbaum/CA_Ch05_PartII.pdf