## Slide 1: ISA (Instruction Set Architecture)
Module-5: Introduction (Lecture-10 & 11)
Prepared by
Amarjeet Kaur

## Slide 2: Instruction Set Architecture
Each processor has its own ISA
Knowledge of ISA is required by:
  Programmers programming at Machine level
  Compiler writers who are translating a high level program to the machine level
  Hardware designers who are responsible for implementing the ISA
ISA is a common target for all compiler writers of different high level languages. JVM is a virtual ISA
Both compiler writers and hardware designers influence the features to be incorporated in ISA design

## Slide 3: ISA ...
An ISA specifies:
  The functionality of the processor (i.e. the set of machine instructions that the processor can handle)
  The hardware components (registers, ALU, flags, program counter etc.) and their internal connection pathways.
Both specifications are interrelated (i.e. functionality is specified in terms of hardware components)
Instructions included in ISA should have the following:
  Cost-effective and efficient (in terms of time taken for execution) implementation through hardware technologies
  Convenience and usefulness at the compilation stage (compiler is able to make good use of it)
ISA specification shows how the machine appears to a machine language programmer (or a compiler writer)

## Slide 4: ISA ....
The hardware may have some components that are of no concern to the programmer and thus are not visible in ISA. Hardware designer would include them for his convenience(like Temp).
Issues in ISA design:
  How many instructions (Data movement, ALU operations and Branching)
  How many operands in an ALU instruction – 0, 1, 2 or 3
  Operands stored where – stack, accumulator, registers, memory
  How operand location to be specified in an instruction (Addressing modes)
  Number and size of programmable registers – general or special purpose
  Memory Address size – storage Little Endian or Big Endian

## Slide 5: ISA ....
  Data types and size
  RISC or CISC
  Instruction Formats (encoding of instructions)
Issues such as whether control unit is microprogrammed or hardwired, or is the processor pipelined, or is it superscalar, are generally of no concern to ISA.
Although some of the above features of microarchitecture may be of use to compiler for exploiting the performance advantage offered by such features.
Out of the above issues following are Instruction related:
  Number of operands in ALU instructions 0, 1, 2, or 3 – Zero (all operands implicit – Stack), one (two operands are implicit – Accumulator), two (one operand is implicit – register), three (no implicit operand – all explicit)

## Slide 6: ISA ....
    Addressing modes – register, indirect, direct, immediate etc.
    Instruction Formats (organization of bits in a machine instruction)
Why registers are used in a CPU?
  Provides a space for storing results avoiding trips to memory
  Gives flexibility to compiler writer – can store variables while evaluating an expression
  Helps in parameter passing
  More efficient for pipelining
  Lesser number of bits are required to mention a register than memory location making instruction length smaller
Machines with registers are called GPR computers
GPR provide more flexibility to compiler writers

## Slide 7: ISA ....
Try evaluating (A*B)-(B*C)-(A*D) on a stack type architecture and a machine with say 4 registers where ALU result can be sent to any register
Classification of GPR machines based on number of operands in ALU instructions
Machine type | No. Of ALU Operands | No. Of Memory Ref. | Example Processors
Reg-Reg | 3 | 0 | MIPS
Reg-Mem | 2 | 1 | Intel x86, Motorola 68000
Mem-Mem | 3 | 3 | VAX(Virtual Address eXtension)

## Slide 8: ISA ...
Reg-Reg (3,0) has :
  Fixed length instructions
  All instructions take about same time to execute
  No addressing modes – easy compilation
  But instruction count for a program increases – more time spent on fetching
Reg-Mem (2,1) has:
  Variable instruction length
  Variable time for execution
  Complex addressing modes
  But smaller instruction count
What information has to go in a machine instruction?

## Slide 9: Elements of a machine instruction
There are three main pieces of information to be given in a machine instruction:
  Operation to be performed (move, add, jump etc.) – Opcode
  Location specifier for each operand – two source, and one result operand
  Next instruction reference
Most of the next instruction reference is implicit
Only in branching instructions, the next address is given
The operands may be in one of the following locations:
  CPU registers
  Immediate (in the instruction itself)
  Main memory
  I/O device

## Slide 10: Instruction representation
Each instruction is represented by a sequence of bits
The sequence is divided into fields – one field for each piece of information as shown below for a 16 bit instruction
When an instruction has been fetched into IR, the control unit has to decode the Opcode field and then take action accordingly .
We use a symbolic representation of machine instructions for convenience of programmers working at machine level.
Opcode is represented as a mnemonic such as LDA, MOV, ADD, JMP, JZ, etc.
Opcode 4 bits | Operand 1 4 bits | Operand 2 4 bits | Operand 3 4 bits

## Slide 11
Hex | Mnemonic | Hex | Mnemonic | Hex | Mnemonic | Hex | Mnemonic
0 | NOP | 50 | MOV D,B | 9B | SBB E | E9 | PCHL
1 | LXI B | 51 | MOV D,C | 9C | SBB H | EA | JPE
2 | STAX B | 52 | MOV D,D | 9D | SBB L | EB | XCHG
3 | INX B | 53 | MOV D,E | 9E | SBB M | EC | CPE
4 | INR B | 54 | MOV D,H | 9F | SBB A | EE | XRI
5 | DCR B | 55 | MOV D,L | A0 | ANA B | EF | RST 5
6 | MVI B | 56 | MOV D,M | A1 | ANA C | F0 | RP
7 | RLC | 57 | MOV D,A | A2 | ANA D | F1 | POP PSW
9 | DAD B | 58 | MOV E,B | A3 | ANA E | F2 | JP
0A | LDAX B | 59 | MOV E,C | A4 | ANA H | F3 | DI
0B | DCX B | 5A | MOV E,D | A5 | ANA L | F4 | CP
0C | INR C | 5B | MOV E,E | A6 | ANA M | F5 | PUSH PSW
0D | DCR C | 5C | MOV E,H | A7 | ANA A | F6 | ORI
0E | MVI C | 5D | MOV E,L | A8 | XRA B | F7 | RST 6
0F | RRC | 5E | MOV E,M | A9 | XRA C | F8 | RM
11 | LXI D | 5F | MOV E,A | AA | XRA D | F9 | SPHL
12 | STAX D | 60 | MOV H,B | AB | XRA E | FA | JM
13 | INX D | 61 | MOV H,C | AC | XRA H | FB | EI
14 | INR D | 62 | MOV H,D | AD | XRA L | FC | CM
15 | DCR D | 63 | MOV H,E | AE | XRA M | FE | CPI
16 | MVI D | 64 | MOV H,H | AF | XRA A | FF | RST 7
Note. Reprinted from “Microprocessor Architecture Programming and Applications with the 8085”, by Ramesh Gaonkar, Prentice Hall, Eight Edition, 2013.

## Slide 12
Hex | Mnemonic | Hex | Mnemonic | Hex | Mnemonic
17 | RAL | 65 | MOV H,L | B0 | ORA B
19 | DAD D | 66 | MOV H,M | B1 | ORA C
1A | LDAX D | 67 | MOV H,A | B2 | ORA D
1B | DCX D | 68 | MOV L,B | B3 | ORA E
1C | INR E | 69 | MOV L,C | B4 | ORA H
1D | DCR E | 6A | MOV L,D | B5 | ORA L
1E | MVI E | 6B | MOV L,E | B6 | ORA M
1F | RAR | 6C | MOV L,H | B7 | ORA A
20 | RIM | 6D | MOV L,L | B8 | CMP B
21 | LXI H | 6E | MOV L,M | B9 | CMP C
22 | SHLD | 6F | MOV L,A | BA | CMP D
23 | INX H | 70 | MOV M,B | BB | CMP E
24 | INR H | 71 | MOV M,C | BC | CMP H
25 | DCR H | 72 | MOV M,D | BD | CMP L
26 | MVI H | 73 | MOV M,E | BE | CMP M
27 | DAA | 74 | MOV M,H | BF | CMP A
29 | DAD H | 75 | MOV M,L | C0 | RNZ
2A | LHLD | 76 | HLT | C1 | POP B
2B | DCX H | 77 | MOV M,A | C2 | JNZ
2C | INR L | 78 | MOV A,B | C3 | JMP
2D | DCR L | 79 | MOV A,C | C4 | CNZ
2E | MVI L | 7A | MOV A,D | C5 | PUSH B
2F | CMA | 7B | MOV A,E | C6 | ADI
30 | SIM | 7C | MOV A,H | C7 | RST 0
31 | LXI SP | 7D | MOV A,L | C8 | RZ
32 | STA | 7E | MOV A,M | C9 | RET
Note. Reprinted from “Microprocessor Architecture Programming and Applications with the 8085”, by Ramesh Gaonkar, Prentice Hall, Eight Edition, 2013.

## Slide 13
Hex | Mnemonic | Hex | Mnemonic | Hex | Mnemonic
33 | INX SP | 7F | MOA A,A | CA | JZ
34 | INR M | 80 | ADD B | CC | CZ
35 | DCR M | 81 | ADD C | CD | CALL
36 | MVI M | 82 | ADD D | CE | ACI
37 | STC | 83 | ADD E | CF | RST 1
39 | DAD SP | 84 | ADD H | D0 | RNC
3A | LDA | 85 | ADD L | D1 | POP D
3B | DCX SP | 86 | ADD M | D2 | JNC
3C | INR A | 87 | ADD A | D3 | OUT
3D | DCR A | 88 | ADC B | D4 | CNC
3E | MVI A | 89 | ADC C | D5 | PUSH D
3F | CMC | 8A | ADC D | D6 | SUI
40 | MOV B,B | 8B | ADC E | D7 | RST 2
41 | MOV B,C | 8C | ADC H | D8 | RC
42 | MOV B,D | 8D | ADC L | DA | JC
43 | MOV B,E | 8E | ADC M | DB | IN
44 | MOV B,H | 8F | ADC A | DC | CC
45 | MOV B,L | 90 | SUB B | DE | SBI
46 | MOV B,M | 91 | SUB C | DF | RST 3
47 | MOV B,A | 92 | SUB D | E0 | RPO
48 | MOV C,B | 93 | SUB E | E1 | POP H
49 | MOV C,C | 94 | SUB H | E2 | JPO
4A | MOV C,D | 95 | SUB L | E3 | XTHL
4B | MOV C,E | 96 | SUB M | E4 | CPO
4C | MOV C,H | 97 | SUB A | E5 | PUSH H
4D | MOV C,L | 98 | SBB B | E6 | ANI
4E | MOV C,M | 99 | SBB C | E7 | RST 4
4F | MOV C,A | 9A | SBB D | E8 | RPE
Note. Reprinted from “Microprocessor Architecture Programming and Applications with the 8085”, by Ramesh Gaonkar, Prentice Hall, Eight Edition, 2013.

## Slide 14: Number of Addresses
Operations are Data movement , or ALU operations, or branching (conditional or unconditional)
Operands are referred as register names, or variable names (actually address in main memory), or constants.
Most architectures have Instructions with one, two or three addresses.
Symbolic representation of ADD instruction
  ADD A, B, C A = B+C 3-address
  ADD A, B A = A+B 2-address
  ADD A AC = AC+A 1-address (accumulator type)
  ADD T = (T-1)+T 0-address (stack type)
where T is top-of-stack

## Slide 15: Write the code to implement the expression A = (B – C)*D on 3-, 2-, 1-, and 0-address machines. Do not rearrange the expression. In accordance with programming language practice, computing the expression should not change the value of its operands.

## Slide 16: Types of operands
Types of data handled at machine level are:
  Addresses
  Numbers
  Characters
  Logical data
Types of Operations
  Data Transfer Typical mnemonic
    Move MOV
    Load LD
    Store ST
    Exchange XCHG
    Clear CLR
    Set SET
    Push / Pop PUSH / POP

## Slide 17: Types of Operations
Arithmetic
  Add ADD
  Subtract SUB
  Multiply MUL
  Divide DIV
  Absolute ABS
  Negate NEG
  Increment INR
  Decrement DCR
Logical
  And AND
  Or OR
  Not NOT

## Slide 18: Types of Operations
    Exclusive-or XOR
    Compare CMP
    Shift Left/Right SHL/SHR
    Rotate Left/Right RAL/RAR
  Transfer of Control
  Jump JMP or BR
  Jump Conditional JZ/JNZ/JN ... Etc
  Jump to subroutine CALL
  Return RET
  Skip SKIP
  Halt HLT
  No operation NOP

## Slide 19: Types of Operation
I/O
  Input IN
  Output OUT
Machine has some System Control instructions also which are used by OS and not the programmer

## Slide 20: Addressing Modes
How to convey the location of operands in an instruction?
Two categories – for data, and for branching address
For Data (illustrated in 2,1 machine for 2nd operand)
  Immediate (data in the instruction) ADD R1, #6; R1=R1+6
  Direct (data in memory) ADD R1, (1000); R1=R1+Mem[1000]
  Register (data in a CPU register) ADD R1, R2; R1=R1+R2
  Register Indirect (data in Memory) ADD R1, (R2); R1=R1+Mem[R2]
  Memory Indirect ADD R1, @(R2); R1=R1+Mem[Mem[R2]]

## Slide 21: Addressing Modes
  Displacement ADD R1, 100(R2); R1=R1+Mem[100+R2]
  Indexed ADD R1, (R2+R3); R1=R1+Mem[R2+R3]
  AutoInc ADD R1, (R2)+; R1=R1+Mem[R2], R2 = R2+d
  AutoDec ADD R1, -(R2); R2 = R2-d, R1=R1+Mem[R2]
In last two addressing modes d is the size of data in an array. These modes are mainly used in stack operations.
In Memory Indirect mode, the R2 register contains the address of address of the data.
Complex addressing modes facilitate direct translation of some high level constructs

## Slide 22: Instruction Formats
The issues are
  What Instruction length, and
  How many bits for each field (Opcode, operand1, operand2 etc.) in the instruction?
Instruction length – fixed or variable
Intel x86 architecture have variable lengths
MIPS, ARM architectures have fixed lengths
Decision of instruction length affected by
  Size of a memory transfer (a byte or a word etc.)
  Memory size (no. of bits in the address)
  Number of operands
  Processor complexity
In most machines, Instruction length is a multiple of bytes i.e. 8,16,24,32 bits etc.

## Slide 23: Instruction Formats
Variable length provides flexibility in addressing capability, but the full instruction may not be fetched in one trip to memory. The Control unit will come to know of it only after some decoding of the instruction.
In fixed length, fetching is smooth and without any decision from Control unit, but complex addressing may have difficulty.
Allocation of bits
For a given instruction length, how to decide the number of bits for each field?
The tradeoff is between
  Number of Opcodes (Opcode length)
  Number and complexity of addressing modes
Opcode length – fixed or variable ?

## Slide 24: Instruction Formats
Bits to be allocated for operands depends on
  Number of operands
  Complexity of addressing modes
  Number of registers in the machine
  Memory address size
The designer has to play a big balancing act!
Opcode Length
If a machine has 100 different opcodes, then what should be the length of Opcode field?
If instruction length is 16 bits fixed, then how many bits are available for specifying the addressing mode of operands?
It may not be possible to specify a memory address in 9 bits?

## Slide 25: Instruction Formats
Imagine a machine with following Instruction Set:
  15 instructions with 3 operands
  14 instructions with 2 operands
  31 instructions with 1 operand
  16 instructions with 0 operand
Instruction length has been fixed at 16 bits
An operand requires 4 bits to specify its addressing mode.
Should we have fixed length Opcode?
If yes, how many bits?
7 ? Then how to accommodate 3 operand instructions?
Solution is variable length Opcodes
4 bit Opcode for 3 operand instructions

## Slide 26: Expanding Opcodes
8 bit Opcodes for 2 operand instructions
12 bit Opcodes for 1 operand instructions
And then all bits for Opcode in the case of 0 operands
Opcode distribution:
Case-A ) 0000 – 1110 for first 15 instructions (3 operand type)
Case-B) Code 1111 indicates that Opcode is 8 bits
1111 0000 – 1111 1101 for 14 instructions (2 operand type)
Case-C) Code 1111 111x indicates that Opcode is 12 bits
1111 1110 0000 – 1111 1110 1111 for 16 instructions
1111 1111 0000 – 1111 1111 1110 for 15 more
Case-D) Code 1111 1111 1111 indicates a 16 bit Opcode
1111 1111 1111 0000 – 1111 1111 1111 1111 for last 16 instructions

## Slide 27: References
https://ocw.mit.edu/courses/electrical-engineering-and-computer-science/6-004-computation-structures-spring-2017/c9/c9s1/#16
M. Morris Mano, Computer System Architecture, Prentice Hall of India Pvt Ltd, 3rd Edition (updated) , 30 June 2017.
William Stallings, Computer Organization and Architecture–Designing for Performance, Ninth Edition, Pearson Education, 2013.
Ramesh Gaonkar, Microprocessor Architecture Programming and Applications with the 8085, Prentice Hall, Eight Edition, 2013.