## Slide 1: “Laser Technology and Applications” 16B1NPH533 Lecture 36
He-Ne laser

## Slide 2
Schematic of Gas Lasers
In gases, energy levels of atoms involved in lasing action are well defined and narrow; broad pump bands do not exist
To excite gaseous atoms; pump sources with sharp wavelengths are required
 Optical pumping not suitable for gas lasers.
Most common method; Electric discharge through the gas medium.
Gas contained in a tube with cavity mirrors.
High DC voltage ionizes the gas
for conduction.
Electrons in the discharge transfer energy to atoms in the gas by collisions.

## Slide 3
First gas laser ever developed; Still one of the most widely used lasers.
  He-Ne: An atomic laser employs Four-level pumping scheme.
    Active Medium; a mixture of 10 parts of He to 1 parts of Ne
    Ne-atoms; active centres- have energy levels suitable for laser transitions
    He-atoms help efficient excitation of Ne-atoms
He-Ne Laser
Schematic of a He-Ne laser with external mirrors
Discharge tube of about 30cm long, 1.5 cm in diameter, filled with a mixture
of He & Ne gases in 10:1 ratio.
Electrodes connected to HV (~10kV) to produce discharge in gas.

## Slide 4
HV of 10kV applied across the gas- ionizes the gas
Electrons & ions accelerated towards anode and cathode
  Electrons being smaller in mass acquire higher velocity
Electrons transfer K.E. to He atoms through inelastic collisions.
He atoms excited to levels F2 & F3 – metastable levels
Transfer energy to Ne-atom through collisions
  Resonant transfer of energy
Possible in He-Ne atoms
Ne-atoms being heavy, could not be pumped up efficiently without He-atoms.

## Slide 5
Role of He-atoms is to excite Ne-atoms and cause P.I.
  Probability to transfer energy from He-Ne is more ;
    10 He per 1 Ne atoms.
  Reverse probability i.e. Ne-He is extremely small
E4 (4s) & E6 (5s) levels in Ne; Metastable States (Accumulation of atoms)
Population inversion between
  E6 and E5 (4p), E3 (3p) levels
  E4 and E3 levels
Lasing takes place & light produced
corresponding to
E6 →E3 laser beam of red colour at 632.8 nm
E4 → E3 laser beam at wavelength of 1150 nm
E6 → E5 laser beam in IR region at 3390 nm
In reality, ~150 laser transitions are possible, however, only three are dominant transitions.

## Slide 6
Ne-atoms in level E3 decays rapidly to E2 (a metastable state)
Accumulation may take place unless removed by some means
  E2 →E1 transition induced by collisions with walls of discharge tube.
    Discharge tube made as narrow as possible to enhance probability of atomic collisions with walls.
E2 level is more likely to be populated by the electric discharge itself
  An increase in population at E2 causes decrease in P.I. →Lasing ceases.
      Current in discharge tube maintained at low level
Reason for not getting high power He-Ne lasers
Major applications as Red light at 632.8 nm
      Resonator mirrors coated with multi-layer dielectric coatings.
        He-Ne laser: Simple, less expansive, practical, high quality beam.
Applications:
      Laboratories, Interferometry, Laser Printing, Bar Code Reader, Scanners, Surface Testing, Surveying, Alignment etc