## Slide 1: ELECTRICAL SCIENCE – 2 (15B11EC211) UNIT – 6 LECTURE 4

## Slide 2: Lecture Overview
Biasing and its need
Operating Point
Different Biasing Circuits
Voltage Divider Bias Configuration
  Load Line Analysis
  Numerical
References

## Slide 3: Biasing Circuit
Biasing is application of dc voltages to establish a fixed level of current and voltage.
Need of Biasing
To turn the device “ON”
To place it in operation in the region of its characteristic where the device operates most linearly .
Improper biasing causes
  Distortion in the output signal
  Clipped output signal

## Slide 4: Important Relationships
I E = IC + I B
I E =(β + 1)I B
β = IC/IB
VCB = VCE - V BE

## Slide 5: Operating Point [2]
For transistor amplifiers the resulting dc current and voltage establish an operating point on the characteristics that define the region that will be employed for amplification of the applied signal.
Because the operating point is a fixed point on the characteristics, it is also called the quiescent point (abbreviated Q-point).
Transistor Regions Operation:
  Linear(Active)-region operation: Base–emitter junction forward-biased Base–collector junction reverse-biased
  Cutoff-region operation: Base–emitter junction reverse-biased Base–collector junction reverse-biased
  Saturation-region operation: Base–emitter junction forward-biased Base–collector junction forward-biased

## Slide 6: Operating Point

## Slide 7: Biasing Circuits
Fixed-bias circuit
Emitter-stabilized bias circuit
Voltage divider bias circuit
DC bias with voltage feedback

## Slide 8: VOLTAGE DIVIDER BIAS CIRCUIT [1]
  Provides good Q-point stability with a single polarity supply voltage.
  This is the biasing circuit wherein, ICQ and VCEQ are almost independent of beta (β).
  The level of IBQ will change with beta so as to maintain the values of ICQ and VCEQ almost same, thus maintaining the stability of Q point.

## Slide 9
  For analyzing a voltage divider bias circuit are:
  1st step: Locate capacitors and replace them with an open circuit
  2nd step: Simplified circuit using Thevenin Theorem
  3rd step: Locate 2 main loops which;
    BE loop
    CE loop

## Slide 10: Simplified circuit using Thevenin Theorem

## Slide 11: BE Loop Analysis

## Slide 12: CE Loop Analysis

## Slide 13: Load Line Analysis

## Slide 14: Numerical [1]
Find Ic & VCE ::

## Slide 16: References
[1] R. Boylestad and L. Nashelsky, ‘Electronic Devices and Circuit Theory’, PHI, 7e, 2001
[2] A. S. Sedra,, and K. C. Smith, ‘Microelectronic Circuits’. Oxford Oxford University Press, 7th Edition, 2012
[3] D.C. Kulshreshtha, ‘Electronic Devices and Circuits’, New Age, 2e, 2006