## Slide 1: ELECTRICAL SCIENCE-1 (15B11EC111) UNIT-4 Lecture-4

## Slide 2: Chapter4 Steady State Analysis of Sinusoid

## Slide 3: Purely Capacitive Circuit
(a) Capacitive circuit.
(b) Voltage and current waveforms.
Next

## Slide 5
(c) Phasor diagram (with V reference).
(d) Phasor diagram (with I reference).
The current leads applied voltage by π/2.
Next

## Slide 6: Analysis
We start with the applied voltage,
v  Vm sint
dt dt
m
 i  C dv  C d (V sin t)
 CVm cos t  CVm cos t
 CVm sin(t  π/2)
If V  V0  V  j0;
I  I90  0  jI
Next

## Slide 7: Power waveform for a purely capacitive circuit.
The average power and the power factor are given as
P  VI cos  VI cos90  0
pf  cos  cos90  0(leading)
Next

## Slide 10
Impedance and Admittance
Impedance is defined as the ratio of the phasor voltage
to the phasor current.

## Slide 12
Admittance is defined as the reciprocal of impedance

## Slide 14: Power and Power Factor
(a) AC source delivering power to a load.
(b) Waveforms of voltage, current and power.
and i  Im sin(t  )
v  Vm sint
Next

## Slide 15: Let the effective values be
V  Vm / 2 and I  Im / 2
Apparently, it seems that the power going to the load should be equal to VI.
But the real power is the average of the instantaneous power.
Let us write the expression of instantaneous power,
Next

## Slide 16
 VI cos VI cos(2t  )
2 2
 I m [cos  cos(2t  )]  VI[cos  cos(2t  )]
2
 Vm
 Vm I m [cos{t  (t  )}  cos{t  (t  )}]
p  vi  [Vm sin t][Im sin(t  )]  Vm Im sin t sin(t  )
The average value of the second term is zero.
Thus, the average power or actual power or real power consumed by the load is given as
P  VI cos
Next

## Slide 17: Power Factor It is defined as the factor by which the apparent power is to be multiplied so as to get the real power. Thus,
power factor ( pf )  cos
In case the phase angle is zero, the circuit is said to have unity pf. The real power is then same as the apparent power.
Next

## Slide 18: Example 3
In an ac circuit, the instantaneous voltage and current are given as
v  55sint V and i  6.1sin (t  / 5) A
Determine the average power, the apparent power, the instantaneous power when t (in radians) equals 0.3, and the power factor in percentage
Next

## Slide 19: Solution : The phase angle,  = π/5 The rms values are
V  Vm  55  38.89 V 2 2
I  Im  6.1  4.31A 2 2
Therefore, the average power,
Pav  VI cos  38.89 4.31cos / 5
 167.62 0.809  135.6 W
The apparent power,
Pa  VI  38.89 4.31  167.62 VA
Next

## Slide 20: The instantaneous power at ωt = 0.3,
p  VI cos VI cos(2t  )
 135.6 167.62cos(2 0.3   / 5)  31.95 W
The power factor,
pf  cos  cos / 5  0.809  80.9%
Next

## Slide 24
References
R.C. Dorf and James A. Svoboda, “Introduction to Electric Circuits”, 9th ed, John Wiley & Sons, 2013.
D.C. Kulshreshtha, Basic Electrical Engineering, Revised 1st ed, Tata Mc Graw Hill, 2017.
V. K.Mehta, Rohit Mehta, Basic Electrical Engineering, 6th ed, S. Chand Publishing, 2012.

## Slide 25: Thanks